## Slide 1: H2O and Temperature by Raman Lidar in the troposphere and in the UTLS above Payerne
5th TOLNet / 2018 NDACC LWG Meeting
G. Martucci1, V. Simeonov2, L. Renaud1, , Fran Navas-Guzman1, Jordan Voirin1, Shannon Hicks3, Sham Gamage3, Bob Sica3, Bertrand Calpini1 and A. Haefele1,3
1 Office Fédérale de Météorologie et Climatologie, MeteoSuisse, Payerne, Suisse
2 EPFL, École Polytechnique Fédérale de Lausanne, Suisse
3 Department of Physics and Astronomy, The University of Western Ontario, London, Canada

## Slide 2: Outline
LIDAR operational calibrated measurements
  Tropospheric PRR temperature
  Tropospheric Raman Water Vapour
Ice cloud characterization by balloon-lidar match experiment.
PRR temperature climatology in the UTLS
Raman Water Vapour climatology in the UTLS
Future activities: OEM retrieval

## Slide 3
Operated in Payerne, Switzerland
Since 2008
Fully automatic Raman lidar
Day and nighttime operation
Narrow FOV and bandwidth
High laser-pulse energy, 450 mJ
The RAman Lidar for Meteorological Observations - RALMO

## Slide 4: Solar background calibration
The procedure to calibrate the RALMO water vapor mixing ratio (ω) consists of the daily automatic correction of the calibration factor C obtained by radiosounding at time t0.
The correction of C is based on an automatic monitoring of the differential aging of the N2 and H2O PMTs using the solar background.
The C(t) factors obtained using the BKG show an excellent agreement with the C(ti) factors within 10% and provide the possibility to characterize RALMO along the entire dataset (9 years) with only one radiosounding calibration (initialization).

## Slide 5
Tropospheric Water Vapour climatology
Since 2008 RALMO has produced on average 1 profile every hour, i.e. 50% availability of tropospheric profiles.

## Slide 6: Tropospheric PRR-Temperature
16-11-2017
19-11-2017

## Slide 7
Cloud 1: in-situ
Opt. Depth (lidar): 0.007 (subvis)
IWC: ~0.1 mg/m3
Cloud 2: liquid origin
Opt. Depth (lidar): 0.15
IWC: ~7.4 mg/m3
clear difference in optical and microphysical properties between two clouds with different origins
Different cirrus origins over Payerne, night of 15-Apr-2015:
first cirrus layer around 9 km of liquid origin
second thin layer around 11.5 km of in-situ origin
Backward trajectories using LAGRANTO [Sprenger & Wernli, 2015] on ERA-INTERIM. Large dots indicate presence of LWC.

## Slide 8
Seeder-feeder effect over Payerne, night of 5-Jul-2011:
Presence of supercooled liquid droplets
indicated by lidar
Homogenously nucleated ‘mother’-cloud (high BR), slowly sedimenting and evaporating in descending air mass
Sedimenting ice particles from the ‘mother’ cloud
Mixed-phase layer (massive BR in lidar), with the water phase being depleted by the falling ice crystals through riming and deposition, thus decreasing the BR over time
Fall streak of ice crystals into subsaturated environment
1.
2.
3.
4.

## Slide 9: PRR temperature climatology in the UTLS
10 km
11 km
13 km

## Slide 10
PRR temperature climatology in the UTLS
ΔT within 1.8-2.5 K compared with the operational SRS-C34
ΔT = RAL- C34

## Slide 11
10 km
11 km
13 km
improvement of PRR temperature in 2017
PRR temperature climatology in the UTLS
ΔT = RAL- C50
ΔT within -0.8, -1 K compared with the operational SRS-C50

## Slide 12: Raman Water Vapour climatology in the UTLS
10 km
11 km
13 km

## Slide 13: Raman Water Vapour climatology in the UTLS
Δω in the 20-30% compared with the operational SRS-C34
Δω = RAL- C34

## Slide 14: Canadian fires aerosols in the UTLS above PAY

## Slide 15: Canadian fires aerosols in the UTLS above PAY
WV = ~200 ppmv @12 km

## Slide 16: Optimal Estimation Method
Bayes’ Theorem:
The measurement y can be expressed through a forward model:
The measurement: y
Measurement noise: e
The state vector: x
Auxiliary parameters: b
The forward model: F
Goal: solve the equation for x

## Slide 17: Future activities: Water Vapour operational OEM Retrieval
Residuals
2012 – 07 – 26 Night Retrieval
Forward model counts – Measurements
Statistical Uncertainty
Radiosonde
Traditional
OEM Retrieval

## Slide 18: Future activities: PRR temperature operational OEM retrieval
20110909 – Clear Night

## Slide 19: Summary
The water vapour mixing ratio is calibrated automatically using the solar background since a year now.
PRR temperature has been affectedly improved since beginning 2017 thanks to software and hardware upgrades.
Cirrus can be characterized by combination of LIDAR and balloon matched-measurements with ice and liquid phase being separated.
RALMO T and WV climatological timeseries well agree with the operational SRS-C34/50 radiosounding in the UTLS.
In 2018/19 the automatic retrieval of T and WV by OEM will be put in place along with the traditional retrievals.