## Slide 1: NDACC Lidar measurements at OHP
S. Godin-Beekmann
NDACC France coordinator
G. Ancellet, P. Keckhut, A. Hauchecorne, S. Khaykin
Lidar PIs

## Slide 2: Outline
Status of the instruments
Some science results except from recent aerosol results (S. Khaykin presentation)
Main issues for lidar operations at OHP
OHP

## Slide 3: Temperature - H2O lidar
Temperature
Time series start in 1979
July 2017 and March 2018 : NDACC LAVANDE intercomparison campaign with the mobile lidar of NASA-GSFC
Since February 2017 : operation in semi automatic mode (manual start, automatic stop). Complete automatic mode foreseen for 2018
Processing of the data at French AERIS data center
Rotational Raman channels (PhD thesis of Yann Caraty) pour temperature measurements in the 0 – 30 km range
Next delivery of data in May 2018.
H2O
Degraded operation of the lidar due to aging filters in the N2 and H2O Raman channels
New filters funded in 2018 and nominal operation foreseen in June 2018
PIs: A. Hauchecorne, P. Keckhut

## Slide 4: Stratospheric and tropospheric ozone DIALs
PIs: G. Ancellet (tropo) and S. Godin-Beekmann (strato)
Stratospheric O3
Time series starts in 1985
Nominal operation up to April 2018: Nd-Yag breakdown Operation should be resumed at the end of May 2018
Contribution to Copernicus Atmosphere Monitoring service
Collaboration with B. Sica’s team for OEM processing of ozone profile (G. Farhani) – Poster presentation at EGU 2018 and paper near ready for submission
Semi-automatic operation mode ready
Tropospheric O3
Time series starts in 1991
Nominal operation
Needs a new more stable laser for semi-automatic mode

## Slide 5: LAVANDE Campaign OHP 2017 - 2018
Intercomparison NDACC campaign NASA (GSFC) mobile lidar
NASA excimer laser breakdown -> :2 periods July 2017 et March 2018
Referee: W. Steinbrecht (DWD)
NDACC Lidar Working Group Huntsville May 2018
Preliminary results

## Slide 6: Temperature profiles from LTA and LiO3S OHP lidars
Median discrepancy over 20 years
Lidar O3 strato – lidar T
Difference < 0.6 K from 30 to 75 km
Wing et al., 2018a, submitted
Comparison with SABER et MLS temperature measurements after satellite altitude adjustment
Wing et al., 2018b, submitted
Temperature lidar @532 nm et 355 nm LIO3s channel Unique comparison of 20 years of data

## Slide 7: Validation of SAGE III/ISS

## Slide 8: Tropospheric ozone trends
NDACC Lidar Working Group Huntsville May 2018

## Slide 9: Issues for lidar operation at OHP
NDACC Lidar Working Group Huntsville May 2018
Strong human resources issues for lidar operation at OHP in the next years:
  5 operators up to 2017
  In 2018 departure of 2 operators
  In 2019 – 2020 departure of station chief
  Discussions with CNRS to get a new technician position
  The position will have to be shared with other atmospheric observation services (ICOS, AERONET)
  Automatization of lidar operation is being performed but it will need refurbishment of LiO3s and LTA telescopes
NDACC-FR involved in European ACTRIS Research Infrastructure project
  Requires proposition of services for O3 lidar community
  Proposal under discussion